Quick Programming Guide

NTS S9000/NX5400

To Program Group Name

- Turn Key to SP position.

- Press 222

- Press X/TIME button.

- Enter group number and the decimal point button.

- Enter name of group up to 10 characters.

- If less than 10 characters press SPACE button after description to the end.

- Press “00” button to print

- Press CASH button to accept description.

- Press CL button twice to exit, and repeat process for next group.

Complete PLU Programming

- Key to SP position

- Press 5201

- Press X/TIME button

- Scan barcode or input own code and press the decimal point button.

- Enter description up to either 16 or 18 characters.

- If less than 16 or 18 characters press SPACE button to the end.

- Press “00” and CASH buttons

- Press X/TIME button 6 times

- Enter group number.

- Press X/TIME button 4 times

- Enter price.

- Press X/times 3 times

- Press CL twice to exit, and repeat process for next PLU.

To Add Stock

- Key to Z2 position

- Scan bar code or input own code and press PLU button.

- Put in stock quantity and press X/TIME button

- Press CL twice to exit

Alternate Method for adding stock

- Key to Z2 position

- Press 406

- Press X/TIME button

- Scan barcode or input own code and press the decimal point button.

- Put in stock quantity and press X/TIME button

- Press CL twice to exit.

To Remove Stock

- Key to Z2 position

- Scan bar code or input own code and press PLU button

- Put in stock quantity to remove and press CR button

- Press CL twice to exit

Alternate Method for removing stock

- Key to Z2 position

- Press 406

- Press X/TIME button

- Scan barcode or input own code and press the decimal point button.

- Put in stock quantity and press CR button

- Press CL twice to exit.

Quick Price Change

- Key to Z1/P position

- Scan bar code or input own code and press PRICE button.

- Put in New price without using decimal point

- Press X/Time button

- Press CL twice to exit.

Alternate Method for quick price changing

- Key to Z1/P position

- Press 305

- Press X/TIME button

- Scan barcode or input own code and press the decimal point button.

- Put in New price without using decimal point

- Press X/Time button

- Press CL twice to exit.

Reports

Full Stock Report

- Key to X position

- Press 42 , X/TIME and CASH buttons.

Individual Item Stock

- Key to X position

- Press 42 and X/TIME button

- Scan bar code or input own code and press decimal point button

- Repeat process for next item

- Pres CASH button to finalize

Cash – In Drawer Report

- Key to X position

- Pres 8 , X/TIME and Cash buttons

Daily Reports

Financial

- Key to Z1/P position

- Press 1 , X/TIME and CASH buttons.

Itemized Sales

- Key Z1/P position

- Press 40 , X/TIME and CASH buttons

Monthly Reports

Financial

- Key to Z2 position

- Press 2 , X/TIME and CASH buttons.

Itemized Sales

- Key Z2 position

- Press 41 , X/TIME and CASH buttons

Date & Time

Date

- Key to X Position

- Press 1

- Press the decimal point button

- Enter YYYYDDMM (Always 8 digits) e.g. 20090112

- Press X/Times

Time

- Key to X Position

- Press 2

- Press the decimal point button

- Enter HHMMSS (Always 6 digits) e.g. 083000

- Press X/Times

Store Logo

1.	Key to SP

2.	Press 122 X/TIMES

3.	Line Number e.g. 1

4.	Press decimal point button

5.	Enter details up to 24 characters

6.	If less than 24 characters, press SPACE button till the end

7.	Press “00” button

8.	Press CASH button

9.	Press X/Times to continue to next line or press CL to exit and repeat the process

Cashier Name

1.	Key to SP

2.	Press 212 X/Times

3.	Press Cashier number e.g. 1 (for cashier 1)

4.	Press decimal point button

5.	Enter cashier name up to 16 characters

6.	If less than 16 characters, press SPACE button till the end

7.	Press “00” button

8.	Press CASH button

9.	Press X/TIMES for next cashier

10.      Press CL to exit and repeat the process

Error Sheet

NTS S9000-01

EE-00 System error: Perform the initial reset operation. If it does not work, disconnect AC cord and contact your distributor.

EE-01 Printer error: Disconnect AC cord and then back on or check the printer. If "printer with automatic cutter [SF-10.h=1] has been set on ECR which has the manual cutter specification, this message is displayed. Perform the initial reset operation, then set 0 to [SF-10.h].

DE-02 Input figure over limitation: Press CL key. (PLU HALO can be omitted temporarily by using HALO RELEASE key)

IE-03 Cashier is not signed on. Press Clerk/Cashier ID, press 1, press Clerk/Cashier ID

UE-14 Drawer is open. (optional drawer open sensor is required)

IE-15 Cash declaration is compulsory. (can be omitted temporarily by using OFF COMPULSORY key)

LE-16 Registration buffer is almost full: Only a few more items can be entered. Prepare to close the transaction.

PE-18 Journal paper near end: Replace with new paper roll. Displays when [SF-2.e=1] is set. (can be omitted temporarily by using OFF COMPULSORY key) Check Journal Roll or placed journal roll correctly

UE-22 Short tendering amount input of TTL 5 prohibited [SF-73.b=1]

EE-30 PLU not found: Enter correct PLU code or program the PLU code.

DE-48 PLU code check digit error: Enter correct PLU code.

DE-49 PLU code price check digit error of in-store marking code: Enter correct PLU code.

UE-51 This PLU is not programmed as a master PLU for Not Found PLU entry

UE-52 Not Found PLU has not been entered

CE-65 Scanner communication error

CE-70 IRC line (RS485) is busy.

CE-71~74 Kitchen printer 1~4 error: Confirm the setting of the printers. Refer to the INTERFACES & PERIPHERALS MANUAL for details.

EE-99 It indicates that ECR data might be collapsed because of a low battery condition by battery discharge while ECR is in stock for a long period. Perform Physical RAM Test and Auto Preset, then leave ECR ON for minimum of 3 hours for battery charge.

. NTS S9000-02

00 System error: Require a initial reset.

01 Printer error: Disconnect AC cord and then back on or check the printer.

02 Input figure over limitation: Press CL key.

(PLU HALO can be omitted temporarily by using HALO RELEASE key.)

03 Clerk is not signed on.

08 Message input is compulsory. (omitted temporarily by OFF COMPULSORY key)

09 Perform foreign currency subtotal display operation: Press F.C. SBTL key and F.C. MEDIA key.

10 Number of persons input is compulsory. (omitted temporarily by OFF COMPULSORY key)

13 Tendered amount input is compulsory. (omitted temporarily by OFF COMPULSORY key)

14 Drawer is open: This message is displayed only when the 'drawer open sensor' is being used.

15 Cash declaration is compulsory. (omitted temporarily by OFF COMPULSORY key)

16 Registration buffer is almost full: Prepare to close the transaction

18 Journal paper near end (displayed by [SF-2.e=1]): Replace with new paper roll. .

(only at the beginning of transaction, it can be released temporarily by using OFF COMPULSORY key)

30 PLU not found: Enter correct PLU code or program the PLU code.

(displayed when Z report or program sequence is performed in the middle of transaction)

48 PLU code check digit error: Enter correct PLU code.

49 PLU code price check digit error of in-store marking code: Enter correct PLU code.

53 This PLU is not programmed as a master PLU for Not Found PLU entry

54 Not Found PLU has not been entered

65 Scanner communication error

67 Channel C communication error

68 Channel D communication error

69 Buffer for journal data transfer is full.

70 IRC line (RS485) is busy.

71-74 Kitchen printer   error:

Confirm the setting of the printers. Refer to the INTERFACES & PERIPHERALS MANUAL for details.

80 ESF memory is full.

81 ECR is in communication with EFT terminal.

82 EFT terminal communication error: Press CL key.

86 Communication time out

99

It indicates that ECR data might be collapsed because of a low battery condition by battery discharge while ECR

is in stock for a long period.

Perform Physical RAM Test and Auto Preset, then leave ECR ON for minimum of 3 hours for battery charge.

For further technical info call on (011) 832 2555

Key to sp turn power on

Hold 456

Put power on